## Slide 1: March 30, 2023 Jakob Krummenacher & Kevin Bourgeois
Carbon Capture and Sequestration at El Dorado, AR Ammonia Plant

## Slide 2: LSB Industries at a glance
Business Overview
  LSB Industries, founded in 1968 and headquartered in Oklahoma City, OK, is a publicly traded company that manufactures and sells chemical products for the agricultural, mining and industrial markets
  $550+m in annual revenue in 2021
  Three production facilities strategically located near customer demand areas
  El Dorado, AR: Manufactures ammonia, ammonium nitrate, nitric acid, sulfuric acid, CO2 and AN solution
  Cherokee, AL: Manufactures UAN, ammonia, AN solution, nitric acid, CO2 and diesel exhaust fluid
  Pryor, OK: Manufactures UAN, ammonia and CO2
LSB is the fifth largest ammonia producer in the U.S.
Chart: 
| Agricultural ($265m) | Industrial ($234m) | Mining ($57m)
Sales | 0.48 | 0.42 | 0.1
Revenue by Business
El Dorado
Cherokee
Pryor
(0.9 MTY)
Ammonia Plant
Urea
AN Solution
UAN
Natural Gas
CO2
Liquifaction
CO2
Nitric Acid
Products sold to market

## Slide 3: Globally a net of 40 Gt of CO2e Greenhouse gas emissions are released into the atmosphere annually
Source: IPCC (Intergovernmental Panel on climate Change), EPA (Environmental Protection Agency)
Buildings - include onsite energy generation and burning fuels for heat in buildings or cooking in homes
Other Energy – include indirect emissions from the energy sector, such as fuel extraction, refining, processing, and transportation
Chart: 
| Electricity and Heat Production | Agriculture, Forestry and Other Land Use | Buldings | Transportation | Industry | Other Energy
Sales | 0.25 | 0.24 | 0.06 | 0.14 | 0.21 | 0.1
Global greenhouse gas emissions by sector
Global greenhouse gas emissions by country
Chart: 
| Other | China | Japan | Russian Federation | India | EU-28 | United States
Sales | 0.3 | 0.3 | 0.04 | 0.05 | 0.07 | 0.09 | 0.15

## Slide 4: Hydrogen and ammonia are expected to be the main carbon-free energy sources in the future
Mobility
Source: U.S. Energy Information Agency
Power & Light
Heating
Renewable Electricity
RNG
Hydrogen
Ammonia
ENERGY TRANSITION TO CLEAN ENERGY
Renewable Electricity
Biomass & RNG
Nuclear
Hydrogen
Ammonia
Renewable Electricity
Biofuels
Hydrogen
Ammonia
NG
Electricity
Heating oil
Propane
Renewable Electricity
RNG
NG
Coal
Nuclear
Renewable Electricity
Biomass
RNG
Gasoline
Diesel
Bunker
Jet Fuel
Electricity
Biofuels
Renewable Electricity
Today
Tomorrow

## Slide 5: Producing low carbon ammonia at El Dorado, AR
Steam Methane Reforming
Ammonia Synthesis
Low-Carbon Ammonia
450kt annually
Carbon Intensity down from 2.2 to 0.9
Process CO2
Nat Gas for heating
H2
N2
Permanent Sequestration
Flue Gas CO2
Nat Gas
Water
Air
Carbon Capture
Pipeline
Agreement with Lapis Energy to develop the CO2 capture and sequestration (CCS) project
Project will receive 45Q tax credits of $85 per metric ton of CO2 sequestered for the first 12 years of operation
Project operations expected to begin by mid 2025, subject to Class VI EPA permitting
Permanently sequestering >450k metric tons of CO2 in saline formations directly under the facility. The sequestered CO2 will reduce the company’s scope 1 GHG emissions by ~25% from current levels

## Slide 6: Lapis Energy
Lapis value proposition
World class subsurface technical team
Entrepreneurial culture built from Kosmos Energy experience
100% capital commitment to FID
Expertise in CCS and energy transition
Proven capital large scale complex project delivery
Unburdened by fluctuations in oil price
Client focused decarbonization
Cresta financial sponsorship
Lapis US Lower 48 Activity
Our purpose is enabling industrial decarbonization through CCS

## Slide 7: How will CO2 be captured and stored at El Dorado?
Smackover
Buckner
Cotton Valley
Hosston
Travis(Peak)
Reynolds
Midway
Wilcox
Woodbine
(Tuscaloosa)
Eagleford
Tokio
Nacatoch
Taylor
Arkadelphia
Cane River
Sparta Aquifer (El Dorado Drinking Water)
surface
critical depth for C02
Seal
Seal
Seal
Seal
Seal
3,000 ft
2
CO2 Injection Zones
4
CO2 Injection Zone
4,000 ft
5,000 ft
6,000 ft
7,000 ft
2,000 ft
1,000 ft
3
1
x
o
o
Injection well
Monitoring well
Monitoring well
o
The reservoirs holding the CO2 are approximately 3500-6500 ft below the surface and 3000 ft below the area drinking water supply.
A 1000 ft thick, impermeable layer of shale separates the injection zone and the area drinking water and prevents any upward migration of CO2
A stringent set of safety requirements will need to be satisfied before the U.S. Environmental Protection Agency (EPA) will give permission to start CO2 injection.
CO2 injection pressures will be very carefully monitored by monitoring wells installed to further ensure integrity
Increasing the number of possible injection zones will reduce the plume size significantly, and thus the need for private pore space rights.

## Slide 8: Seismicity considerations
seismic line A
seismic line B
No copies or screen captures allowed of this slide for copyright reasons
2D Seismic
Purchased 2D seismic grid to constrain structural model and demonstrate lack of faulting
PSTM re-processing to increase imaging quality
Very low seismic activity, no subsurface faults near the LSB property which could be reactivated

## Slide 9: Managing the CO2 plume for 50 years post injection
Smackover
Cotton Valley 1, 2 & 3
Hosston
After 5-year injection
After 50-year post injection
Models include dissolution, but not hysteresis (would reduce plume size further)
4 injection intervals provide redundancy if one or two zones are not connected to enough pore volume, or the plume expands too aggressively
Consider injecting longer (5-10 years) in some of the Cotton Valley intervals if well connected
Smackover has a large plume size because of high permeabilities, salinities & Kv/Kh - excluded

## Slide 10: Proposed monitoring scheme and injection well
In-zone monitoring
plume and pressure
In-zone monitoring
plume and pressure
Above injection zone plume and pressure monitoring
Injection Well
Firm-up well locations, based on final dynamic modelling
Supplement subsurface monitoring with indirect monitoring; 4D VSP, 4D sparse array seismic or 4D 2D
Once plume hits a deep monitoring well a new deep monitoring well will have to be drilled further away to track further plume expansion, or injection will have to be moved up to the next zone
EPA well construction requirements are aimed to protect the USDW and provide zonal isolation
EPA cementing and casing requirements
Initially two deep monitoring wells and one shallow monitoring location, one injection well

## Slide 11: Schematic of the CO2 capture facility
COMPRESSOR
STAGE 1-3
TEG DEHYDRATION
COMPRESSOR
STAGE 1-3
COMPRESSOR
STAGE 4-5
COMPRESSOR
STAGE 4-5
AMMONIA PLANT GENERATING CO2
BLOWER
SUBSURFACE
INJECTION PLANT
CO2 COMPRESSION AND DEHYDRATION PLANT

## Slide 12: Location of the capture facility and CO2 pipeline
Compressor Plant
CO2 Supply
CO2 Injection
New pipe rack
Existing pipe rack
Bridge over tracks
Bridge over road
Bridge over road
Bridge over pond
Well ~400m S of plant

## Slide 13: Project Timeline
Complete Feasibility
Secure pore space
Class VI well submittal
Finance & tax equity FEED
Class VI injection
submittal
Class VI Well Permit EPA Interchange
2
Months
Startup injection
Subsurface & Class VI Permit
Financial Structuring
Land, Regulatory & ESG
Engineering Design & Construction
Commercial
1
5
6
Class VI Injection approval
Final Dynamic Model
6
2
Incorporate well data into report
Final submittal
Commissioning
Initial submittal
~2Q 2022
Funding & Closing
TE commitment
Final plume model
3
7
Drilling
~3Q 2022
Progress Class VI
4
~1Q 2023
~1Q 2024
~4Q 2024
~1H 2025
~4Q 2022
9
12
24
40
32
Class VI approval to construct
EPA engagement
Class VI Injection Permit EPA Interchange
Class VI Well Design
Plume Model (final)
Plume Model (prelim.)
Pore Space
Define Land Rights
ESG stakeholder engagement
Tax Equity and Debt
Financing Commitments
Tax Equity Prelim DD
FEED
Drill Wells
Capture Facility Construction
Concept Engineering
Commercial Agreements
Order long lead items
Detailed Engineering
Expecting injections to start in 1H 2025

## Slide 14
Questions?
LSB Industries – EL Dorado Chemical Plant